BOILER PRE-STARTUP CHECK LIST

DELAYS:

IF, WHEN ARRIVING AT THE JOBSITE OUR SUPPORT TECHNICIAN IS DELAYED IN STARTING EQUIPMENT OR HAS TO RETURN TO THE JOB DUE TO ANY OF THE ITEMS BELOW BEING INCOMPLETE/FALISFIED OR, FOR ANY REASON NOT THE RESPONSIBILITY OF RYAN COMPANY INC., EXPENSES INCURRED WILL BE CHARGED BACK TO THE REQUESTER.

Contracting Company:_______________________________________________

Job: _____________________________________________________________

Address:

Boiler Model:  						 Serial #:

Boiler Model:  						 Serial #:

Boiler Model:  						 Serial #:

Modsync Model:  					 Serial #:

Start-up service will not be scheduled until this form is completed, signed and returned to us.

GENERAL

1. Is boiler in building and piping completed ________________

2. Is smoke stack or breeching completed per manual________________

3. Are blow-down or drain valves piped ________________

4. Is water make-up to boiler piped ________________

5. Has boiler been filled with water and leak tested________________

6. Are feed water or circulating pumps connected and operating  ________________

GAS FIRED BOILERS

1. Is gas meter installed and what PSI into building________________

2. Is gas piping completed, sized correctly meeting boiler requirements, lines bleed and leak tested________________

3. Is gas regulator installed ________________

4. Is inlet gas or propane pressures correct to appliances and what are they ________________

INSTALLATION FOR PULSE

1. Are flex lines installed on gas inlets, water inlets and outlets____________

2. Are spring isolation hangers installed on the air intake and exhaust flue venting_____

3. Is the boiler mounted on Fulton authorized cubes or springs_____________

OIL FIRED BOILERS

1. Is oil pump installed ________________

2. Is oil piping completed per manual ________________

3. Is oil pump motor and starter wired ________________

4. Do you have a check valve and strainer installed at pump

Suction and also a check valve at oil tank suction ________________

5. Has oil system been thoroughly checked for suction leaks ________________

6. Has oil pump motor rotation been checked ________________

ELECTRICAL SERVICE

1. Is system wiring completed ________________

2. Is power wiring completed ________________

3. Has blower motors rotation been checked ________________

4. Has control wiring for lead lag or BMS been tested____________

SYSTEM LOAD

Is system complete so that full load can be placed on boiler ________________

This is very important.

SAFETY

Is boiler accessible and free of construction debris (trip hazards)___________

OWNER’S OPERATOR

Is the owner’s engineer available for boiler operating instructions after start up is complete. ________________

Will the Mechanical Contractor have someone at the job ________________

PLEASE write below the name of the Job Foreman or Superintendent who our technician

should contact at the job:

Name: ____________________________________Phone #: _________________

ABOVE COMPLETED BY:______________________________________

DESIRED STARTING DATE:____________________________________

If you have any questions please contact Michael McMonagle 952-767-7065 for assistance. We will be happy to assist in any way to avoid any delays in startup.

Please return this complete form via email to Michael (mac@ryancompanyinc.com).

Ver. 3// 9/4/2013

# Text boxes

RYAN COMPANY, INC.

3361 Republic Avenue ( St. Louis Park, MN 55426

Telephone (952) 915-6475 ( (800) 966-9058 ( Fax (952) 915-6480

www.ryancompanyinc.com